| South River Machar Fire Department Standard Operational Guideline | S.O.G. 3:005 |
| --- | --- |
| Section: Fire Ground Operations | Subject: Driveway Lay |
| Date: June 2, 2014 | Page 1 of 2 |

1:00	Purpose

1:01	To provide fast efficient water supply to the fire ground for continuous fire suppression and rescue efforts.

2:00	Scope

2:01	This guideline applies to all firefighting personnel and allied agencies working with	South River Machar Fire Department during the incident or training exercise.

3:00	Procedure

3:01	Fire Apparatus must be sent out in the following order Pump 3, Pump 4, Tank 1, Rescue 2.

3:02	Fire suppression that requires more than 300 Gpm will require mutual aid for 1 additional tanker in addition to the automatic aid agreement with the Sundridge Strong Fire Department.  Mutual aid will also be required where there is an extended distance from the water source to the fire ground (more than 5 km).

3:03	Incident Command when possible should assign a Water Commander to coordinate tanker movement, staging and dumping.

3:04	Water Command would be the only firefighter involved in water shuttle operations to communicate with the Incident Commander.

3:05 	The Water Commander when established is responsible for keeping a log of all water tanker movement.

4:00	Set Up

4:01	Upon arriving on scene Pump 3 completes size up, identifies water supply requirements and tactical objectives.  A brief size up report is to be radioed to Dispatch.

4:02	Pump 3 stops where the port-a-tanks are to be set up and deploys two 3” supply lines, two 4” hard suction lines, portable pump, fuel tank, port-a-tank adapter, mallet then proceeds to the fire ground.

4:03	Pump 4 connects to 1 of the 3” supply lines and nurse pumps to Pump 3.  Once Pump 4 is out of water it immediately returns to the fill site and begins shuttling water.

4:04	While pump 4 is nurse pumping, Tanker 1 sets up its port-a-tank (connecting the portable pump prior to filling the port-a-tank).

4:05	Tanker 1 immediately proceeds to refill once it empties its load.

4:06	If additional water is required for fire suppression a second portable pump is to be deployed top feed Pump 3.

6:00	Responsibility

6:01	It is the responsibility of all Firefighter’s involved in the emergency or training exercise to ensure this guideline is followed in its entirety.

6:02	It is the responsibility of the Commander’s to ensure the guideline is adhered to in its entirety.

6:03	It is the responsibility of the incident commander to ensure that all equipment used during the call is replaced, cleaned, refuelled as required to be ready for the next call.  Equipment that is damaged or lost will be documented on the call sheet and white board.

| Fire Chiefs Signature |  | Date | June 2, 2014 |
| --- | --- | --- | --- |