| South River Machar Fire Department Standard Operational Guideline | S.O.G. 3:010 |
| --- | --- |
| Section: Fire Ground Operations | Subject: Flashover |
| Date: January 6, 2011 | Page 1 of 2 |

1:00	Purpose

1:01	To ensure the proper use of fire streams to help the fire department provide effective and efficient fire suppression as well as enhancing the safety of firefighters performing fire suppression.

2:00	Scope

2:01	This guideline applies to all firefighting personnel and allied agencies working with	South River Machar Fire Department during the incident or training exercise.

3:00	Nozzle Streams and Flow Rates

3:01	Solid stream direst attack is the preferred nozzle pattern when performing interior firefighting operations.  Direct attack will help reduce the amount of air forced into the fire area and will help reduce the amount of steam generated.

3:02	Indirect or combination attack should be used when firefighters are unable to enter the the structure or fire area.

3:03	The minimum flow rate for interior firefighting operations on residential type buildings is 150 Gpm.

3:04	The minimum flow rate for fires in commercial buildings is 250 Gpm.

3:05	Search and Rescue crews that will not be assigned fire suppression tasks may utilize   1 ½”  (38mm) or 1 ¾” (45mm) for commercial buildings to provide limited protection for themselves while not hindering their search efforts as much as larger medium diameter hose such as 2 ½” or 3” would.

4:00	Required Rate of Flow

4:01	The required rate of flow should be reached within the first 2 minutes of firefighting operations.  The Required Rate of Flow is not cumulative and must be achieved to successfully knock down the fire.

4:02	To calculate the required rate of flow (Length x Width x Height / 100)

5:00	Water Supply

5:01	Mutual aid will be utilized in all situations where the water supply is inadequate to meet the required rate of flow.

6:00	Responsibility

6:01	It is the responsibility of all Firefighter’s involved in the emergency or training exercise to ensure this guideline is followed in its entirety.

6:02	It is the responsibility of the Commander’s to ensure the guideline is adhered to in its entirety.

| Fire Chiefs Signature |  | Date | January 6, 2011 |
| --- | --- | --- | --- |