| South River Machar Fire Department Standard Operational Guideline | S.O.G. 3:011 |
| --- | --- |
| Section: Fire Ground Operations | Subject: Safe Roof Operations |
| Date: July 25, 2013 | Page 1 of 2 |

1:00	Purpose

1:01	To ensure that firefighters working on roof operations are doing so in as safe manor as possible.

2:00	Scope

2:01	This guideline applies to all firefighting personnel and allied agencies working with	South River Machar Fire Department during the incident or training exercise.

3:00	Response

3:01	A minimum of 3 firefighters should be committed to roof operations prior to any firefighters accessing the roof.

3:02	1 firefighter of the crew assigned to roof operations will remain on the ground and be assigned the roll of roof sector commander.

3:03 	Roof ladders should be used whenever feasible.

3:04	At least 2 portable radios should be deployed to roof operations, 1 radio should be assigned to the commander and the other to the firefighters on the roof.  Firefighters must radio the incident commander prior to accessing the roof.

3:05	Firefighters must sound there path of travel with irons while operating on the roof and frequently reassess sounding the roof to ensure the structural integrity of the roof.

3:06	Whenever possible a second means of egress should be provided for firefighters on the roof.

3:07	Roof operation crews should ensure they have all of the required equipment prior to entering the roof to help minimize the amount of time on the roof.

3:08	Firefighters should never enter onto a lightweight construction roof if there is any exposure to fire.

4:00	Personal Protection

4:01	Firefighters performing roof operations must be wearing full bunker gear with SCBA and be on air while they are performing roof ooperations.

4:02	R.I.T should be established as soon as possible when roof operations are being performed.

4:03	Incident Command must assess the roof as best as possible prior to assigning firefighters to enter onto the roof.  The integrity of the roof must be continually assessed throughout the roof operations.  The assessment of the roof should include but not limited to construction type, duration and intensity of fire exposure, roof loading  and the condition of the roof prior to the fire.

5:00	Training

5:01	All firefighters performing roof operations must be trained and familiar with the use of ground ladders in addition to the tasks they are assigned such as ventilation.

5:02	It is the responsibility of the firefighters assigned to roof operations to inform the Incident Commander their level of training and their comfort level with roof operations.

6:00	Responsibility

6:01	It is the responsibility of all Firefighter’s involved in the emergency or training exercise to ensure this guideline is followed in its entirety.

6:02	It is the responsibility of the Commander’s to ensure the guideline is adhered to in its entirety.

| Fire Chiefs Signature |  | Date | July 25, 2013 |
| --- | --- | --- | --- |