| South River Machar Fire Department Operational Guidelines | O.G. 3:013 |
| --- | --- |
| Section: Fire Ground Operations | Subject: Municipal Water Supply |
| Date: June 13, 2011 | Page 1 of 2 |

1:00	Purpose

1:01	To provide a means of supplying the fire ground with the best possible water supply available from the municipal water distribution system or other water sources readily available.

2:00	Scope

2:01	This guideline applies to all firefighting personnel and allied agencies working with	South River Machar Fire Department during the incident or training exercise.

3:00	Procedure

3:01	Pump 4 responds to the incident with a 4 firefighter crew and completes size up and starts initial attack.

3:02	Pump 3 responds with a 2 firefighter crew to set up water supply for Pump 4.  The crew from Pump 3 will stay together until they have completed setting up the water supply or until otherwise directed by the Incident Commander.

3:03	If more water will be required Pump 3 lays a reverse lay to the highest capacity hydrant available.  If the distance to the hydrant is greater than 300’ Pump 3 will relay pump to Pump 4, less than 300’ Pump 3 will connect Pump 4 directly to the second hydrant.

4:00	Static Water Supply

4:01	When there is a reliable static water supply located with in 600’ of Pump 4 it should be utilized.

4:02	When the municipal fire hydrants are unable to meet the required rate of flow; a water shuttle should be set up to support fire suppression operations. Water shuttle set up should be established in accordance with SOG 3:017 Supplemental Water Supply and 3:005 Water Shuttle Operations.

4:00	Training

5:01	When training requires the use of water for from the municipal water distribution system only hydrants approved for use for training will be used, if other hydrants are required approval must be obtained from the Public Works Chief Operator of the Village of South River or hi/her designate.

5:02	To reduce the impact on the municipal water distribution system pre-approved fire hydrants should be used whenever feasible to refill fire apparatus water tanks.

5:03	Whenever a municipal fire hydrant is operated and there is a potential risk of the hydrant freezing the Public Works Chief Operator of the Village of South River or hi/her designate shall be notified.

6:00	Responsibility

6:01	It is the responsibility of all Firefighter’s involved in the emergency to ensure this guideline is adhered to in its entirety.

6:02	It is the responsibility of the Commander’s to ensure this guideline is adhered to in its entirety.

6:03	It is the responsibility of the incident commander to ensure that all equipment used during the call is replaced, cleaned, refueled as required to be ready for the next call.  Equipment that is damaged or lost will be documented on the call sheet and white board.

| Fire Chiefs Signature |  | Date |  |
| --- | --- | --- | --- |