| South River Machar Fire Department Operational Guidelines | O.G. 3:017 |
| --- | --- |
| Section: Fire Ground Operations | Subject: Supplemental Water Supply |
| Date: July 9, 2011 | Page 1 of 2 |

1:00	Purpose

1:01	To provide a means of supplying the best possible water supply available for fire suppression when the required fire flows exceed the capabilities of the water distribution system.  This guideline should be considered for all Commercial, Industrial, Multi-Residential and Single family dwellings with exposures.  This guideline should also be considered for all fires West of Eagle Lake Road and North of Ottawa Avenue as well as all fires on Kilper Dr, Johnson Drive, Spruce Street, Poplar Street and Grant Court.

2:00	Scope

2:01	This guideline applies to all firefighting personnel and allied agencies working with	South River Machar Fire Department during the incident or training exercise.

3:00	Procedure

3:01	Pump 4 responds to the incident with a 4 firefighter crew and completes size up and starts initial attack.

3:02	Pump 3 responds with a 2 firefighter crew to set up water supply for Pump 4 using the best available hydrant.

3:03	If the anticipated fire flows are believed to exceed the capabilities of the water distribution system, Pump 3 crew will proceed to Dublin Street to set up a filling station.  1 Firefighter from Pump 3 crew will remain at the filling station to assist in filling tanker units.

3:04	Tanker 1 should be deployed into water shuttle operations.

3:07	As soon as possible a water supply sector should be established with a Water Command assigned and positioned near the port-a-tank.

3:06	Communications for water shuttle operations should be done on the Mutual Aid channel.

4:00	Automatic Aid

4:01	Automatic Aid units from Sundridge Strong Fire Department should be directed to set up a port-a-tank in an appropriate area, preferably away from the attack pumper.  A portable pump should be deployed to pump the water from the port-a-tank to the attack pumper.

4:02	Automatic Aid Tanker and Pumper Tanker should be put into water shuttle operations.

4:00	Mutual Aid

5:01	Once established that the fire flows will exceed the capacity of the water distribution system Mutual Aid should be activated as follows

- Sundridge Strong Fire Department for additional staffing

- Powassan Fire Department for Tanker Support and staffing

- Burks Falls District Fire Department on standby for Tanker support and staffing

5:02	Mutual aid coordinator must be notified at (705) 472-1221

6:00	Responsibility

6:01	It is the responsibility of all Firefighter’s involved in the emergency to ensure this guideline is adhered to in its entirety.

6:02	It is the responsibility of the Commander’s to ensure this guideline is adhered to in its entirety.

6:03	It is the responsibility of the incident commander to ensure that all equipment used during the call is replaced, cleaned, refueled as required to be ready for the next call.  Equipment that is damaged or lost will be documented on the call sheet and white board.

| Fire Chiefs Signature |  | Date |  |
| --- | --- | --- | --- |